## Slide 1
In the greater physics world, a vital question exists, what links the classical and quantum worlds together? At what point is something big enough to obey classical properties or small enough to remain in the quantum realm? Ideas such as tunnelling exists only in the quantum world and gravity is only relevant in the classical world. My experiment revolves around this question in mind, and it begins with lasers and Gallium Arsenide (GaAs). GaAs is a commonly used semiconductor, meaning it is relatively bad at both conducting and insulating, but there are ways that could possibly make for a good conductor. Semiconductors have a band gap, which requires work to overcome, and the valence electrons must be excited to conquer such a gap. Metals that are naturally conductive have valence electrons that overlap the conduction band already so, naturally, they are conductive; but semiconductors must have some external energy added for its valence electrons to achieve it. For GaAs specifically, the gap is 1.42 eV, which means that for GaAs to become a highly conductive metal, it must have at least 1.42 eV of energy added so the electrons are excited enough.
The lasers used for the experiment were 670 and 780 nm respectively, and the second one generated enough photon energy to roughly 1.59 eV. So, the 780 nm laser should excite the valence electrons in the GaAs enough to breach the band gap which in turn make it a very conductive metal.
Laser effect on Gallium Arsenide Conductivity
Patrick Brien, Raul Puente, Arjun Krishnan, Herman Batelaan
Department of Physics & Astronomy, University of Nebraska-Lincoln
This material is based upon work supported by the
National Science Foundation under Grant No. 2051059.
Introduction
a. This diagram to the left shows the
Conduction band, and the gap in between
Representing the amount of energy needed
to overcome it
1
Scientific Setup
First, we set the laser in place and a place where it should hit. When that is set up, we can use mirrors to adjust the direction of the laser and that will allow it to aim directly at the GaAs target. We also must suspend the GaAs using something that it may stick to, shown in the diagram below.
I also had a setup which used an infrared laser that aimed towards the target as well. However, the GaAs target this time was supported with two small claw tools which connect directly to the DMM.
670 nm red laser
mirrors
telescope
cylindrical lens
mounted GaAs sample
780 nm IR laser
Digital Multimeter
(DMM)
Results
Sponsored by
Based on the given information, the application of the laser to the GaAs should have reduced the resistance by easily twofold, but that was not the case. Upon the 670nm laser application, the resistivity did not change at all, it fluctuated naturally due to its semiconductor properties but there was no significant change. I then decided to apply the 780 nm laser, creating a different setup for it. This laser is over 40x stronger, averaging at 70 mW compared to the 1.5mW average of the 670 nm. Even with this laser hitting the GaAs sample, the resistivity did not change. These are the numbers generated below.
Table with resistivity measurements in Ohms/Ω (670 nm laser)
Table with resistivity measurements in Ohms/Ω (780 nm laser)
Having observed this information, the experiment did not quite yield what we may have expected. The lasers should have had at least some significant impact on the resistivity of the given GaAs sample when shone upon. There may be a multitude of reasons to why there was no expected effect. Possibilities of the hardware of the experiment messing up, such as a dirty GaAs sample, short circuit, diluted silver glue, if it is doped or not, an oxidation layer, supergluing it incorrectly, soldered incorrectly were all tested and there were seemingly no hardware inconsistencies. For the first two samples though given on the tables above, these were with p-doped ones, and I believed that corrected that and using an undoped one for the third sample may have fixed it. The undoped sample does have a much higher resistance though which seems more like semiconductor, which is good. After having shone the laser on the GaAs, it has been observed in other experiments, that the resistance decreases by a very significant amount. A laser of 780nm wavelength should have decreased the resistance by at least 90%2 . This was a surprise as the experiment seemed as if nothing was wrong but there was no change in the resistance regardless is there was a laser shining on it or not.
Sample # | Trial 1 | Trial 2 | Trial 3 | Initial resistance
1st | 128.7 | 142.2 | 146.2 | 143.5
2nd | 25.7 | 25.7 | 25.6 | 25.8
3rd | >2E7 | >2E7 | >2E7 | >2E7
Sample # | Trial 1 | Trial 2 | Trial 3 | Initial resistance
1st | 139.5 | 136.5 | 142.0 | 143.5
2nd | 22.9 | 23.5 | 22.9 | 25.8
3rd | >2E7 | >2E7 | >2E7 | >2E7
[2] Zandi, Omid, "Design and Construction of a High-Current Femtosecond Gas-Phase Electron Diffraction Setup" (2017). Theses, Dissertations, and Student Research: Department of Physics and Astronomy.
Potential Mishaps
This experiment is a replication of a previous experiment done at UNL. The physical mishaps that were described in the previous
panel could not have interfered as I double checked and met with my PI. This experiment was meant to work but there was
something in the way that did not allow the resistance to change. All potential physical problems were solved and the experiment
still did not work. The ending laser has been heavily thinned from the telescope though and the power that is carries in a given
area has been reduced by the initial power. This may be one reason to why there was no observed change, as the telescope was
to fully bathe the sample in the laser. This would make it so the electrical current go through properly, but it may have been too
weak so possibly having a smaller sample and keeping the laser as concentrated as possible may have gotten the resistance to
decrease.
Conclusion
References
[1] Syed Naeem Ahmed, ”Physics and Engineering of Radiation Detection (Second Edition)” 2015.
Using lasers to change the conductivity of GaAs has been unsuccessful, but that does not deter potential changes in the future. While most hardware inconsistencies may have been resolved, there was one problem that may have affected the result that was not able to be resolved.
Future work:
The telescope diluted the laser, and the concentration naturally went down. There may be a possibility that if I hadn’t used a telescope and kept the power concentrated, the higher density may have applied more power and allowed for the electrical current to pass due to less resistance. The problem with removing the laser is that the point is TOO small and would not reach both sides of the current, as that would be necessary to pass the current.
a.
d.
e.
b.
b. Red laser experiment setup
c.
c. Infrared laser experiment setup
d. The current look at the experiment. The laser was widened and while it does bathe the entirety of the GaAs sample, it may have been too weak after having gone through the telescope
e. A look at the experiment that I propose. The sample size of the metal must be reduced heavily but a concentrated laser may still bathe the entirety of the sample and retain its power. This way, it may have enough power to change the resistance value of the GaAs